Generic Tier 2 Quality Assurance Project Plan (QAPP) For

water quality monitoring

SAMPLING AND ANALYSIS ACTIVITIES

January 2015

Alaska Department of Environmental Conservation

Division of Water

The Generic Tier 2 QAPP was developed to cover a wide water quality monitoring sampling and analysis activities.  All sections are intended to be adapted and customized to the specific needs of the individual project while retaining the overall QAPP structure.

Note:	All blue text is for instructional purposes only.  Please delete as you complete your QAPP.

Suitability:	This template is to be used as a guide for developing project specific Quality Assurance Project Plans (QAPPs) for:  Alaska’s Clean Water Actions (ACWA) Grants, Total Maximum Daily Load (TMDL), Domestic Wastewater, Alaska Pollutant Discharge Elimination System (APDES) and Compliance Permits.  Tier 2 water quality monitoring QAPPS are to be designed with a necessary level of rigor to demonstrate compliance with Alaska Water Quality Standards (AWQS).  Providing the prescribed requested information and following this format as defined will assure that sufficient quality assurance and quality control procedures are designed into the project to lead to reliable and defensible monitoring data sufficient for showing compliance with AWQS.

- PROJECT MANAGEMENT ELEMENTS

## A.1 	Title and Approvals:

Title:	Generic Tier 2 Quality Assurance Project Plan for Water Quality Monitoring Sampling and Analysis Activities

Name:	 				Project Manager	Phone:

Organization Name:						email:

Signature:  ______________________________		Date:	______________

Name:	 				Project QA Officer	Phone:

Organization Name:						email:

Signature:  ______________________________		Date:	______________

Name:	                                  DEC DOW Project Manager   Phone:

ADEC DOW Program Name:					email:

Signature:  ______________________________		Date:	______________

Douglas Kolwaite ADEC DOW QA Officer	Phone:            (907) 465-5305

ADEC DOW Tech Services Program				email:	douglas.kolwaite@alaska.gov

Signature:  ______________________________		Date:	______________

## A.2 	TABLE OF CONTENTS

A.1 	Title and Approvals:	2

A.2 	TABLE OF CONTENTS	3

A.3	DISTRIBUTION LIST	5

A.4	PROJECT TASK/ORGANIZATION	6

A.5	PROBLEM DEFINITION/BACKGROUND AND PROJECT OBJECTIVES	8

A.5.1	Problem Definition	8

A.5.2	Project Background	8

A.5.3	Project Objective(s)	9

A.6	PROJECT/TASK DESCRIPTION and SCHEDULE	9

A.6.1	Project Description	9

A.6.2	Project Implementation Schedule	10

A.7	DATA QUALITY OBJECTIES AND CRITERIA FOR MEASUREMENT DATA	11

A.7.1	Data Quality Objectives (DQOs)	11

A.7.2	Measurement Quality Objectives (MQOs)	11

A.8 	SPECIAL TRAINING REQUIREMENTS/CERTIFICATION	16

B.	DATA GENERATION AND ACQUISITION	18

B.1	SAMPLING PROCESS DESIGN (Experimental Design)	18

B.1.1	Define Monitoring Objectives(s) and Appropriate Data Quality Objectives	18

B.1.2	Characterize the General Monitoring Location/s	18

B.1.3	Identify the Site-Specific Sample Collection Location(s), Parameters to be measured and frequencies of collection	19

B.2	SAMPLING METHOD REQUIREMENTS	20

B.2.1 	Sample Types	20

B.2.2	 Sample Containers and Equipment	21

B.2.3	 Sampling Methods	22

B.3	SAMPLE HANDLING AND CHAIN OF CUSTODY REQUIREMENTS	23

B.3.1	Sampling Procedures	23

B.3.2	Sample Custody Procedures	23

B.3.3	Shipping Requirements	23

B.4	ANALYTICAL METHODS AND REQUIREMENTS	23

B.5	QUALITY CONTROL REQUIREMENTS	23

B.5.1	Field Quality Control (QC) Measures	24

B.5.2	Laboratory Quality Control (QC) Measures	24

B.6	INSTRUMENT/EQUIPMENT TESTING, INSPECTIONAND MAINTENANCE REQUIREMENTS	26

B.7	INSTRUMENT CALIBRATION AND FREQUENCY	26

B.8	INSPECTION/ACCEPTANCE OF SUPPLIES AND CONSUMABLES	26

B.9	DATA ACQUISITION REQUIREMENTS (NON-DIRECT MEASUREMENTS)	27

B.10	DATA MANAGEMENT	27

B.11              Data Storage and Retention	28

C.	 ASSESSMENTS	29

C.1	ASSESSMENTS AND RESPONSE ACTIONS	29

C.2	REVISIONS TO QAPP	31

C.3	QA REPORTS TO MANAGEMENT	32

D.	DATA VALIDATION AND USABILITY	32

D.1	DATA REVIEW, VERIFICATIONAND VALIDATION REQUIREMENTS	32

D.1.1	Data validation	33

D.1.2	Data Verification	33

D.1.3	Data Review	33

D.2	VERIFICATION AND VALIDATION METHODS	33

D.2.1	Validation Methods	33

D.2.2	Verification Methods	34

D.3	RECONCILIATION WITH USER REQUIREMENTS	34

LIST OF ABBREVIATIONS

ACWA		Alaska’s Clean Water Actions

ADEC			Alaska Department of Environmental Conservation

APDES		Alaska Pollutant Discharge Elimination System

ASTM			American Society for Testing and Materials

AWQMS		Ambient Water Quality Monitoring System

BETX			Benzene, Ethylbenzene, Toluene, Xylenes (m, р, ο)

CWA			Clean Water Act

COC			Chain of Custody

cfu/100mL		coliform forming units/100 milliliters

DMR			Discharge Monitoring Report

DMRQA sample	Discharge Monitoring Report Quality Assurance sample

DQO			Data Quality Objective

DO			Dissolved Oxygen

DROPS		Discharge Reporting and Online Permitting System

EPA			Environmental Protection Agency

GPS			Global Positioning System

ICIS-NPDES	Integrated Compliance Information System – National Pollutant Discharge and Elimination System

IDL	Instrument Detection Limit

MQO			Measurement Quality Objective

MDL			Method Detection Limit

MSDS			Material Safety Data Sheet

mS/cm			microsiemens/centimeter

mg/L			milligrams/liter

μg/L			micrograms/liter

ND			Non Detect

NELAC		National Environmental Laboratory Accreditation Counsel

PE Sample		Performance Evaluation Sample

PT Sample		Performance Test Sample

PQL			Practical Quantification Limit

QA			Quality Assurance

QAP			Quality Assurance Plan

QAPP			Quality Assurance Project Plan

QC			Quality Control

QMP			Quality Management Plan

RL			Reporting Limit

RPD			Relative Percent Difference

RSD			Relative Standard Deviation

SPAR			Spill Response and Recovery

SOP			Standard Operating Procedure

STORET		Storage and Retrieval System

TAH			Total aromatic hydrocarbons

TMDL			Total Maximum Daily Load

VOC			Volatile Organic Compounds

WA DOE		Washington State Department of Ecology

WQS			Water Quality Standards

## A.3	DISTRIBUTION LIST

List the names and addresses of those who receive copies of the approved QAPP and subsequent revisions in Table 1.

| Table 1 Distribution List |
| --- |
| NAME | POSITION | AGENCY/ Company | DIVISION/ BRANCH/SECTION | CONTACT INFORMATION |
|  | Project Manager |  |  | Phone: Email: |
|  | Project Quality Assurance Officer |  |  | Phone: Email: |
|  | Sampling Manager |  |  | Phone: Email: |
|  | Lab Manager |  |  | Phone: Email: |
|  | Data Manager |  |  | Phone: Email: |
|  | Lab QA Manager |  |  | Phone: Email: |
|  | Project Manager | ADEC | Division of Water/ | Phone: Email: |
| Douglas Kolwaite | QA Officer | ADEC | Division of Water/ Tech. Services/QA | 907-465-5305 Douglas.kolwaite@alaska.gov |
|  |  |  |  | Phone: Email: |

## A.4	PROJECT TASK/ORGANIZATION

List the duties and responsibilities of key individuals and organizations participating in the monitoring project in Table 2:

| Table 2 Project Organizational Responsibilities |
| --- |
| Position Title | Agency or Company | Division Branch/Section | Responsibilities |
| Project Manager | Add project info | Add project info | Revise as appropriate Responsible for overall technical, financial and contractual management of the project and subsequent reporting of QA reviewed (validated and verified) data to DEC. |
| Project QA Officer | Add project info | Add project info | Revise as appropriate Responsible QA review and approval of plan and to ensure all monitoring complies with the QAPP specified criteria. This is accomplished through routine technical assessments of the sample collection, analysis and data reporting process. Assessments may include, but are not limited to: on-site field audits, data audits, QA review of blind lab performance evaluation samples, lab audits, etc. These assessments are performed independent of overall project management. |
| Sampling & Analysis Manager | Add project info | Add project info | Add project responsibilities |
| Field Sampling staff | Add project info | Add project info | Add project responsibilities |
| Laboratory Manager | Add project info | Add project info | Responsible for the overall review and approval of contracted laboratory analytical work, responding to sample result inquiries and method specific details. Responsible for QA/QC of laboratory analysis as specified in the QAPP and reviews and verifies the validity of sample data results as specified in the QAPP and appropriate EPA approved analytical methods. |
| Laboratory Quality Assurance Manager/Officer | Add project info | Add project info | Laboratory Quality Assurance Manager/Officer – Responsible for QA/QC of water quality laboratory analyses as specified in the QAPP. Along with Laboratory Manager, the Lab QA Officer reviews and verifies the validity of sample data results as specified in the QAPP and appropriate EPA approved analytical methods. |
| Project Manager | ADEC | Division of Water | Responsible for overall technical and contractual management of the project. For Permit related monitoring projects, responsible for ensuring permittee complies with permit required water quality monitoring as specified in the approved QAPP |
| Water Quality Assurance Officer | ADEC | Division of Water | Responsible for QA review and approval of plan and oversight of QA activities ensuring collected data meets project’s stated data quality goals |

Figure 1, Project Organizational Structure, as appropriate for the monitoring project.  Be sure to use separate identifying lines to discriminate from each other the following:  management direction, data reporting and QA assessment/reporting.

## A.5	PROBLEM DEFINITION/BACKGROUND AND PROJECT OBJECTIVES

### A.5.1	Problem Definition

In this section clearly state the specific problem to be solved, decision to be made, or outcome to be achieved.

### A.5.2	Project Background

Provide a brief background summary for the purpose of the monitoring project. Include sufficient information to provide historical, scientific and regulatory perspective. If previous monitoring data exists and is relevant to proposed monitoring project, provide summary of results in Table 3 along with the appropriate numeric ADEC water quality standard/s (pollutant concentration: e.g., ground water, surface water, aquatic life freshwater, aquatic life marine water, etc).  Explain how this data was used to rationalize the proposed monitoring plan.

Revise Table 3 as appropriate for the monitoring project.

| Table 3 Example Summary Table of Previous Project Relevant Monitoring Data |
| --- |
| Site Location | Date | Measurement Parameter | Alaska WQS |
|  |  | Analyte | Conc. | Meas. units | Aquatic Life | Recreational/ Drinking Water |

### A.5.3	Project Objective(s)

In this section define the overall objectives for this monitoring project.  Clearly state what is the purpose for collecting monitoring data, why it is being collected and how this data will be used to support the project’s objectives?  If there are regulatory requirements governing the reason/s for collecting monitoring data, cite the specific federal and/or state statue/s.  State how the proposed monitoring plan fulfills this requirement?

## A.6	PROJECT/TASK DESCRIPTION and SCHEDULE

### A.6.1	Project Description

Provide a summary paragraph describing the work to be performed.

In Table 4, list the parameters to be measured and recorded.

| Table 4 Parameters to be Measured |
| --- |
| Field Measurements | Laboratory Measurements |

Samples may be analyzed in the field or in a laboratory.

Note 1:	 ADEC certifies laboratories for drinking water and contaminated sites analysis only.  At the present time, ADEC does not certify laboratories for water/wastewater analyses.  However, an ADEC drinking water-approved laboratory lends credibility to a laboratory’s quality assurance and quality control processes.  A list of ADEC-approved microbiological laboratories is available at: http://dec.alaska.gov/applications/eh/ehllabreports/certmicrolabs.aspx

and for laboratories providing chemical analysis at:  http://dec.alaska.gov/applications/eh/ehllabreports/certchemlabs.aspx

Note 2:	For microbiological analyses, only a laboratory with current ADEC drinking water certification that resides within Alaska may be used.  Due to the short sample holding time (< 8 hours), labs outside of Alaska would not reasonably be able to receive and start the analysis as specified by the EPA water/wastewater approved microbiological method.

Note 2:	For labs contracted outside of Alaska, it is strongly recommended that the contracted laboratory have either NELAC and/or State certification (e.g., Washington State Department of Ecology), for the respective water/waste water analytical methods.

In this section include the name and accreditation of contracted laboratory

Insert a large scale map, or multiple maps, showing the overall geographic location/s of field tasks. (Note in section B1, Sampling Process Design, include larger scale topographic map(s) identifying specific geographic location(s) of sampling sites).

### A.6.2	Project Implementation Schedule

Revise Table 5 as appropriate to describe the project implementation schedule.

| Example Table 5 Project Implementation Schedule |
| --- |
| Product | Measurement/ Parameter(s) | Sampling Site | Sampling Frequency | Time Frame |
| QAPP Preparation |  |  |  |  |
| Field Sampling | DO, pH, Temp, Cond. Turbidity, Fecal Coliforms | River Road Mile 3 Site #1, upstream side of culvert, above outfall | Weekly | June – Sept |
|  | DO, pH, Temp, Cond., Turbidity, Fecal Coliforms, TAHs | River Road Mile 3 Site #2, downstream side of culvert below outfall | Weekly randomized sample timeframe | June – Sept |
|  | DO, pH, Temp, Cond., Turbidity, Fecal Coliforms, TAHs | Site # 3, Mile 3 River Road, Downstream of bridge | Weekly, randomized sample timeframe | June – Sept |
| Lab Analysis | Fecal Coliforms | All sites | Analyses within sample holding time requirements | June - Sept |
| Field Audit | Audit of field monitoring operations | All sites | < 30 days of project start-up | 1/project |
| Data Analysis |  |  |  |  |
| Data Review |  |  |  |  |
| Data Report |  |  |  |  |

## A.7	DATA QUALITY OBJECTIES AND CRITERIA FOR MEASUREMENT DATA

### A.7.1	Data Quality Objectives (DQOs)

Data Quality Objectives (DQOs, EPAQA/G4).  DQOs are qualitative and quantitative statements derived from the DQO Process that:

Clarify the monitoring objectives (i.e., determine water/wastewater pollutant concentrations of interest and how these values compare to water quality standards regulatory limits).

Define the appropriate type of data needed.  In order to accomplish the monitoring objectives, the appropriate type of data needed is defined by the respective AWQS.  For pollutants, compliance with the AWQS is determined by specific measurement requirements.  The measurement system is designed to produce water pollutant concentration data that are of the appropriate quantity and quality to assess compliance.

### A.7.2	Measurement Quality Objectives (MQOs)

Measurement Quality Objectives (MQOs) are a subset of DQOs.  MQOs are derived from the monitoring project’s DQOs.  MQOs are designed to evaluate and control various phases (sampling, preparation, and analysis) of the measurement process to ensure that total measurement uncertainty is within the range prescribed by the project’s DQOs.   MQOs define the acceptable quality (data validity) of field and laboratory data for the project.  MQOs are defined in terms of the following data quality indicators:

- Detectability

- Precision

- Bias/Accuracy

- Completeness

- Representativeness

- Comparability

Detectability is the ability of the method to reliably measure a pollutant concentration above background.  DEC DOW uses two components to define detectability: method detection limit (MDL) and practical quantification limit (PQL) or reporting limit (RL).

- The MDL is the minimum value which the instrument can discern above background but with no certainty to the accuracy of the measured value.  For field measurements, the manufacturer’s listed instrument detection limit (IDL) can be used.

- The PQL or RL is the minimum value that can be reported with confidence (usually some multiple of the MDL).

Note:	The measurement method of choice should at a minimum have a practical quantification limit or reporting limit 3 times more sensitive than the respective DEC WQS and/or permitted pollutant level (for permitted facilities).

Sample data measured below the MDL is reported as ND or non-detect.  Sample data measured ≥ MDL but ≤ PQL or RL is reported as estimated data.  Sample data measured above the PQL or RL is reported as reliable data unless otherwise qualified per the specific sample analysis.

Precision is the degree of agreement among repeated measurements of the same parameter and provides information about the consistency of methods.  Precision is expressed in terms of the relative percent difference (RPD) between two measurements (A and B).

For field measurements, precision is assessed by measuring replicate (paired) samples at the same locations and as soon as possible to limit temporal variance in sample results.  Overall project precision is measured by collecting blind (to the laboratory) field replicate samples. Laboratory precision is determined similarly via analysis of laboratory duplicate samples. For paired and small data sets, project precision is calculated using the following formula:

Where:	 RPD = relative percent difference

A = primary sample

B = replicate field sample or laboratory duplicate sample

For larger paired precision data sets (e.g. overall project precision) or multiple replicate precision data, use the following formula:

RSD = 100*σ/mean

Where:	RSD = relative standard deviation

σ = standard deviation

k = number of paired replicate samples (A and B)

d = A - B

A = primary sample

B = replicate field sample or laboratory duplicate sample

Bias (Accuracy) is a measure of confidence that describes how close a measurement is to its “true” value.  Methods to determine and assess accuracy of field and laboratory measurements include, instrument calibrations, various types of QC checks (e.g., sample split measurements, sample spike recoveries, matrix spike duplicates, continuing calibration verification checks, internal standards, sample blank measurements (field and lab blanks), external standards), performance audit samples (DMRQA, blind Water Supply or Water Pollution PE samples from American Association for Laboratory Accreditation (A2LA) certified, etc.  Bias/Accuracy is usually assessed using the following formula:

Completeness is a measure of the percentage of valid samples collected and analyzed to yield sufficient information to make informed decisions with statistical confidence.  As with representativeness, data completeness is determined during project development and specified in the QAPP.  Project completeness is determined for each pollutant parameter using the following formula:

T – (I+NC) x (100%) = Completeness

T

Where T = Total number of expected sample measurements.

I = Number of invalid sample measured results.

NC = Number of sample measurements not completed (e.g. spilled sample, etc).

In this section list project data completion criteria for all analytes to be measured.

Representativeness is determined during project development and specified in the QAPP.  Representativeness assigns what parameters to sample for, where to sample, type of sample (grab, continuous, composite, etc.) and frequency of sample collection.

## Comparability is a measure that shows how data can be compared to other data collected by using standardized methods of sampling and analysis.  Comparability is shown by referencing the appropriate EPA CWA approved measurement method as specified in federal and/or state regulatory guidance documents for the parameter/s to be sampled and analyzed (e.g., Alaska Water Quality Standards (http://www.dec.state.ak.us/water/wqsar/wqs/index.htm), EPA Guidelines Establishing Test Procedures for the Analysis of Pollutants Under the Clean Water Act; National Primary Drinking Water Regulations; National Secondary Drinking Water Regulations; and Analysis and Sampling Procedures (http://www.access.gpo.gov/nara/cfr/waisidx_05/40cfr136_05.html), etc). As with representativeness and completeness, comparability is determined during project development and must be specified in the QAPP.

For each parameter to be sampled/measured, list the measurement method to be used and the MQOs to meet the overall data quality objectives.  This applies to both direct field measurements (e.g., field pH meters, DO meters, etc.) as well as samples collected for subsequent laboratory analyses.

This section is to be presented in table format along with the appropriate WQS numerical value!  Use Table 6 format on following page to present MQO information.  Revise as appropriate for the monitoring project.  The project contracted laboratory may be a useful resource for determining the specific values to be included in Table 6.  Laboratory and instrument specific MQO may differ from the example values in Table 6.  For field measurements the manufactures SOP may be a useful reference.

| Table 6 Example: Project Measurement Quality Objectives (MQOs) |
| --- |
| Group | Analyte | Method | MDL (µg/L) | PQL (µg/L) | Alaska WQS | Precision (RPD) | Accuracy (% Recovered) |
|  |  |  |  |  | Aquatic Life | Recreation/Drinking Water |  |  |
| VOCs | Benzene | EPA 602a | 0.33 | 1.0 |  | 10 µg/lb |  | 10 | 86-126 |
|  | Toluene | EPA 602a | 0.46 | 1.5 |  |  |  | 15 | 52-148 |
|  | Ethylbenzene | EPA 602a | 0.35 | 1.2 |  |  |  | 20 | 60-140 |
|  | Xylene, total | EPA 602a | 0.82 | 3.0 |  |  |  | 20 | 60-140 |
| Settleable Solids | Settleable Solids | EPA 160.5 | 0.2 ml/L/hr | 0.2 ml/L/hr | No measureable increase above natural condition |  | <5% increase in 0.1 mm to 0.4 mm fine sediment for waters with anadromous fish; <30% by weight of fines in gravel beds | NA | NA |
| Water Quality | DO (dissolved oxygen) | In situ (electronic probe) EPA 360.1 | NA | (0.01 mg/L | >4.0 mg/L | >7 mg/l for anadromous fish; >5 mg/l for non-anadromous fish; < 17 mg/L | ±20% | NA |
|  | pH | In situ (electronic probe) EPA 150.1 | NA | ±0.01 pH units | 6.5 - 8.5; not vary by 0.5 from natural condition | 6.5 - 8.5 | ±0.1 pH units | ±0.1 pH units |
|  | Temperature | In situ (electronic probe) EPA 170.1 | NA | 0.1°C | <20°C Migration routes < 15°C Spawning areas < 13°C Rearing areas < 15°C Egg /fry incubation < 13°C | <30°C | ±0.2°C | ±0.2°C |
|  | Conductivity | In situ (electronic probe) EPA 120.1 | NA | 0-1: 0.001 1-10: 0.01 10-100: 0.1 (mS/cm) | NA | NA | ± 10% | ± 10% |
| Total Recoverable Inorganics | Aluminum | EPA200.8 | 0.33 | 1.0 | 750 (g/L Acute; 87 (g/L chronic | NA | 20 | 80-120 |
|  | Iron | EPA200.7 | 2.7 | 50 | NA Acute; 1000 (g/L chronic | NA | 20 | 80-120 |
| Dissolved Inorganics | Arsenic | EPA200.8 | 0.044 | 0.15 | 340 (g/L Acute; 150 (g/L chronic | 0.018 (g/L | 20 | 80-120 |
|  | Cadmium | EPA200.8 | 0.062 | 0.20 | Hardness Dependentc | NA | 20 | 80-120 |
|  | Copper | EPA200.8 | 0.034 | 0.10 | Hardness Dependentc | 1300 (g/L | 20 | 80-120 |
|  | Lead | EPA200.8 | 0.030 | 0.10 | Hardness Dependentc | NA | 20 | 80-120 |
|  | Mercury | EPA245.1 | 0.05 | 0.2 | 1.4 (g/L Acute; 0.77 (g/L Chronic | NA | 20 | 80-120 |
|  | Zinc | EPA200.8 | 0.08 | 0.25 | Hardness Dependentc | 7400 (g/L | 20 | 80-120 |
| Hardness | Hardness | 2340B | 1000 | 1000 | NA | NA | 5 | 100 |
| Nutrients | Nitrogen, Total Kjeldahl | 4500-NH3C | 112 | 400 | NA | NA | 30 | 80 - 120 |
|  | Total Phosphorous | 4500 PE/4500-PB | 25.7 | 51.4 | NA | NA | 8 | 80 - 120 |
| Fecal Coliforms | Fecal Coliforms | EPA1604 | 1cfu/100mL | 1cfu/100mL | NA | 100 FC/100 mL | 5 | 95 - 105 |

NA = None available.

a	EPA Method 602 for screening BETX.  If BETX measured, confirm with EPA method 624 (GCMS).

b	Total Aromatic Hydrocarbons  are BTEX (Benzene, Toluene, Ethylbenzene, and Xylene) only.

c	Metal standards for the protection of aquatic life are hardness dependent, the formulas for calculating the appropriate standard are available at: http://dec.alaska.gov/water/wqsar/wqs/index.htm Water Quality Criteria Manual for Toxics (December 12, 2008) Appendix A

## A.8 	SPECIAL TRAINING REQUIREMENTS/CERTIFICATION

Describe in this section any specialized training or certifications needed by personnel in order to successfully complete the project.  Describe how training is to be provided and how the necessary skills are assured and documented, as well as how the organization implementing the data collection is qualified and competent.  Training may be formal or obtained by “mentoring” provided by senior staff, and by coordination with the sub-contracted laboratory.  Revise Table 7 as appropriate to summarize project training.

Sub-contracted laboratories performing analytical work must have the requisite knowledge and skills in execution of the analytical methods being requested.  Information on laboratory staff competence is usually provided in each lab’s Quality Assurance Plan (QAP).  The agency and/or organization implementing the monitoring project is responsible to ensure that the contracted lab maintains on file with the ADEC DOW QA Officer a current copy (electronic preferred) of the laboratory’s QAP.

| Table 7 Example: Project Training/Certification |
| --- |
| Specialized Training/Certification | Field Staff | Lab Staff | Monitoring Supervisor | Lab Supervisor | Project QA Officer |
| Safety training | X | X | X | X | X |
| Water sampling techniques | X |  | X |  | X |
| Instrument calibration and QC activities for field measurements | X |  | X |  | X |
| Instrument calibration and QC activities for laboratory measurements |  | X |  | X | X |
| QA principles |  |  | X | X | X |
| QA for water monitoring systems |  |  | X |  | X |
| Chain of Custody procedures for samples and data | X | X | X | X | X |
| Handling and Shipping of Hazardous Goods | X | X | X | X | X |
| Specific Field Measurement Methods Training | X |  | X |  | X |
| ADEC Microbiological Drinking Water Certification | Certification for microbiological analysis is limited to the individually certified analyst. |
| Lab Analytical Methods Training |  | X |  | X | X |

A.9 	DOCUMENTS AND RECORDS

Revise Table 8 as appropriate to list project specific documents and records.  Include all documents and records that will be produced, their disposition, including location and retention time. Use the following categories to list appropriate documents and records.  Record and document types are examples only.

| Table 8 Project Documents and Records |
| --- |
| Categories | Record/Document Types | Location | Retention Time |
| Site Information | Network Description |  |  |
|  | Site characterization file |  |  |
|  | Site maps |  |  |
|  | Site pictures |  |  |
| Environmental Data Operations | QA Project Plan |  |  |
|  | Field Method SOPs |  |  |
|  | Field Notebooks |  |  |
|  | Sample collection/measurement records |  |  |
|  | Sample Handling & Custody Records |  |  |
|  | Chemical labels, MSDS sheets |  |  |
|  | Inspection/Maintenance Records |  |  |
| Raw Data | Lab data (sample, QC and calibration) including data entry forms |  |  |
| Data Reporting | Discharge Monitoring Reports (DMRs) for permitted facility |  |  |
|  | Progress reports |  |  |
|  | Project data/summary reports |  |  |
|  | Lab analysis reports |  |  |
|  | Inspection Report |  |  |
| Data Management | Data management plans/flowcharts |  |  |
|  | Data algorithms |  |  |
| Quality Assurance | Control charts |  |  |
|  | Data quality assessments |  |  |
|  | DMRQA and PE samples |  |  |
|  | Site audits |  |  |
|  | Lab audits |  |  |
|  | QA reports/corrective action reports |  |  |
|  | Response |  |  |
|  | Performance Evaluation Samples |  |  |

In addition to any written report, data collected for a project will be submitted electronically to ADEC via a CD ROM, ZIP Disk or email ZIP file.  All dates are to be formatted as “MM-DD-YYYY”.

# B.	DATA GENERATION AND ACQUISITION

## B.1	SAMPLING PROCESS DESIGN (Experimental Design)

In this section provide a thorough description of the following three major activities:

- Define the monitoring objective(s) and appropriate data quality objectives.

- Characterize the general monitoring location(s).

- Identify the site specific sample collection location/s, parameters to be measured and frequency of collection.

### B.1.1	Define Monitoring Objectives(s) and Appropriate Data Quality Objectives

In this section describe in sufficient detail such that a person, knowledgeable with water quality monitoring but unfamiliar with the monitoring site and history, clearly understands the project’s breadth, scope, underlying rationale and monitoring plan design assumptions.  Describe how these monitoring objectives relate to the appropriate data quality objectives.

Note:	 If the proposed project plan is as a result of previous monitoring efforts, the previous data is to be summarized in table format including parameters and concentrations measured, methods employed and how the results relate to the Alaska water quality standards criteria. Provide reference to previous data report if available or attach as appendix.

## B.1.2	Characterize the General Monitoring Location/s

In this section provide a description of the monitoring locations and the rationale for their selection.  Be sure to include a map providing an overview of all monitoring locations.  Use Table 9 to identify sample sites and to describe the rationale for their selection.

| Table 9 Site Location and Rationale |
| --- |
| Site ID | Latitude | Longitude | Site Description and Rationale |

## B.1.3	Identify the Site-Specific Sample Collection Location(s), Parameters to be Measured and Frequencies of Collection

In this section describe site specific sampling locations, specific parameters to be measured, type of sample(s) to be collected and frequency of collection and representativeness of scale. Be sure to include topographic map(s) showing each monitoring site with sufficient gradient relief detail to characterize the watershed and how each sample site is representative of the monitoring project’s stated goals.  Identify any structures or obstructions affecting sample collection and potential sources of pollutant contamination.

Note 1: Consider in the design plan how samples are to be collected to best represent environmental conditions of concern (e.g., consider how the temporal and spatial variables of sample collection may provide differing results based upon sample collection times, sample depth and location within water (stream, lake, etc.) boundaries).

Note 2: In baseline monitoring, sample site locations should be determined to ensure both temporal and spatial representativeness.  If possible, samples should be taken directly from the water body, rather than from a container filled from the water body.

Note 3: When water samples are taken in response to water pollution complaints, care should be taken to ensure the sampling sites are both representative of the pollution event and characterize the extent; e.g., collecting samples at the suspect pollution site, and above and below it.

Note 4: When a sample is taken at a wastewater facility discharge outfall, a volume of water equal to at least ten times the volume of the sample discharge line will first be discharged into a bucket or similar container to clear the line of standing water and possible contamination.

Use Table 10 to identify key “Site Representativeness” criteria for each site selection.

| Table 10 Criteria for Establishing Site Representativeness |
| --- |
| Site ID | Monitoring Purpose | Criteria for Site Selection |

Use Table 11 to define the key parameters to be measured, types of samples (in situ measurements, grab, composite, etc.), numbers of samples and collection frequency.

| Table 11 Sampling Schedule (Parameters, Sample Type, Frequency) |
| --- |
| Site ID | Parameters to be measured | Sample Type (I, G, C, etc.) | Sampling Frequency | Sample Time | Total number measurements |
| I ≡ In Situ Measurement G ≡ Grab Sample C ≡ Composite Sample |

Insert detailed map(s), (topographic, batholitic, etc.) identifying location of all monitoring sites.  Map(s) should be of sufficient clarity and resolution of scale to represent each individual sampling site along with buildings, structures and topographic features (water bodies, elevation change, etc) and point sources of pollution that could possibly influence quality of the water bodies to be monitored.

## B.2	SAMPLING METHOD REQUIREMENTS

Project sampling staff should wear disposable gloves and safety eyewear, if needed, and observe precautions while collecting samples. Sampling staff need to be aware of the potential chemical and biological hazards present.  The Project Sampling Staff collecting samples must take care not to touch the insides of bottles or lids/caps during sampling.

### B.2.1 	Sample Types

Samples will be listed as “composite” or “grab” on the Chain-of- Custody or Transmission Form and in field logbook or field data sheets.

### B.2.2	 Sample Containers and Equipment

In this section describe specific sample handling and custody requirements (If the results of a sampling program may be used as evidence, a strict written record (Chain of Custody) must be documented tracking location and possession of the sample/data at all times).

All sampling equipment and sample containers must be cleaned according to the equipment specifications and/or the analytical laboratory.  Bottles supplied by a laboratory are pre-cleaned, must never be rinsed, and will be filled only once with a sample.

For samples requiring cooling preservation, a temperature blank shall accompany each cooler (min/max thermometer preferred).  Any min/max thermometer used shall be readable to at least 0.2°C.

Use Table 12 to list specific analyte/method criteria for required parameter holding times and preservation methods.  Revise Table 12 as appropriate for the monitoring project. For parameters not listed in this table, see 40 CFR 136 Table II-Required Containers, Preservation Techniques, and Holding Times

| Example Table 12 Preservation and Holding Times for the Analysis of Samples |
| --- |
| Analyte | Matrix | Container | Necessary Volume | Preservation and Filtration | Maximum Holding Time |
| Residue (settleable solids) | Surface Water | P, FP, G | 1 L | Cool <6oC, do not freeze | 48 hours |
| BTEX | Surface Water | G with FP lined septum | 120 mL (3-40mL) | HCl to pH < 2; < 6°C, do not freeze | 14 days |
| Cu, Cd, As, Pb (Dissolved) | Surface Water | P, FP, G | 250 mL | Filtered within 15 minutes of collection using a 0.45 µm filter; HNO3 to pH < 2 | 6 months |
| Cu, Cd, As, Al, Pb (Total Recoverable) | Surface Water | P, FP, G | 250 mL | HNO3 to pH < 2 | 6 months |
| Nitrate-Nitrite | Surface Water | P, FP, G | 1 L | Cool <6oC; H2SO4 to pH < 2, do not freeze | 28 Days |
| Total Phosphorous | Surface Water | P, FP, G | 1 L | Cool <6oC; H2SO4 to pH < 2, do not freeze | 28 Days |
| Fecal Coliform | Surface Water | G, PA | 250 mL | Cool <10oC; do not freeze, 0.0008% Na2S2O3 | 6 hours 2 hrs lab prep (note: time not additive) |
| Hardness | Surface Water | P, FP, G | 100 mL | HNO3 to pH < 2; < 4°C, do not freeze | 6 months |

P = polyethylene, FP = flouropolymer, G = glass, PA = autoclavable plastic

### B.2.3	 Sampling Methods

This section provides general guidance on how to collect different types of samples.  Delete those sections not appropriate for the type of samples to be collected.  If specific sample collection methods will be followed, cite the appropriate source/method or else include in this section a detailed description of the sampling method to be followed.

Surface Water Samples, Streams -

Sampling stations should always be located in the main stream channel.  Since stream waters are usually well mixed vertically, often subsurface sampling at a convenient depth is adequate for collection of representative samples at a given point.  Subsurface samples are taken within the upper meter or may be a composite of two or more strata.  The sampler should be aware of thermal stratification due to discharges or tributaries.

Lakes, Ponds, Reservoirs-

A sufficient number of stations should be established in random locations to define adequately the parameters of concern.  Usually the deepest part of the lake should be included as one of the stations.  Where concentrations of chemical or physical parameters can vary with depth, samples should be collected from all major depth zones, or water masses.  In shallow waters (2 to 3 m), samples shall be collected at 0.5 to 1 m.  In deeper water (> 3 m), samples should be collected at regular depth intervals.

Grab Samples – Sample bottles will be filled sequentially, to the shoulder of the bottle, leaving a small space for expansion and mixing. Note that some sample types, such as VOC and fecal coliform bacteria have specific bottle filling requirements.  The laboratory will provide sampling instructions with the sample bottles.  If necessary, samplers will consult with the laboratory regarding sampling procedures.

Composite Samples – Samples will be composited directly into the sample.  Between composite subsets, bottles will be kept in a cooler with ice to reach and maintain a sample temperature of 4 +/-2°C.  The time of the initial portion of the composite, composite intervals, and the final compositing time must be noted in the field logbook or data sheets.  Sample time listed on the Chain of Custody (COC) or Transmission Form and the sample bottle must be the time of the final sample composite portion.

## B.3	SAMPLE HANDLING AND CHAIN OF CUSTODY REQUIREMENTS

### B.3.1	Sampling Procedures

See Section B.2 of this QAPP – Sampling Method Requirements

### B.3.2	Sample Custody Procedures

In this section describe any chain of custody (COC) procedures if required.  Include example COC form and COC SOP as an appendix to the QAPP.

### B.3.3	Shipping Requirements

Packaging, marking, labeling, and shipping of samples will comply with all regulations promulgated by the U. S. Department of Transportation in 49 CFR 171-177.  Staff should receive the necessary training for shipping samples or consult with the laboratory for shipping instructions.

Temperature preservation method and holding time limitations must be considered when decisions are made regarding sampling and shipping times for time and temperature sensitive sample analytes.

## B.4	ANALYTICAL METHODS AND REQUIREMENTS

In this section reference the laboratory’s Quality Assurance Plan (QAP) and applicable SOPs for each method analyte to be measured.  If the lab has a current QAP and relevant SOPs on file with ADEC DOW QA Officer, these can be specifically referenced in this section.  If not, it is responsibility of the monitoring project manager to ensure the lab’s QAP and relevant SOPs are included (as attachments) to the monitoring project’s QAPP.

Monitoring shall be conducted in accordance with EPA-approved analytical procedures and in compliance with 40 CFR Part 136, Guidelines Establishing Test Procedures for Analysis of Pollutants.  Reference the Project’s MQO table (section A7) of this QAPP for list of parameters of concern, approved analytical methods, method-specific detection and reporting limits, accuracy and precision values applicable to this project.

Under direction of the Project Manager, project staff will ensure that all equipment and sampling kits used in the field and laboratories use EPA CWA approved methods. The project’s QA officer will verify that only EPA CWA approved methods (or in specific incidences ADEC DOW pre- approved methods) are used.

## B.5	QUALITY CONTROL REQUIREMENTS

Quality Control (QC) is the overall system of technical activities that measures the attributes and performance of a process, item, or service against defined standards to verify that they meet the monitoring project’s data quality objectives.

In this section define the QC activities that will be used to control the monitoring process to validate sample data.  Use separate tables to define field QC measurements and Lab QC measurement and their criteria for accepting/rejecting project specific water quality measurement data.

### B.5.1	Field Quality Control (QC) Measures

QC measures in the field include but are not limited to:

- Proper cleaning of sample containers and sampling equipment.

- Maintenance, cleaning and calibration of field equipment/kits per the manufacturer’s and/or        laboratory’s specification, and field SOPs.

- Chemical reagents and standard reference materials used prior to expiration dates.

- Proper field sample collection and analysis techniques.

- Correct sample labeling and data entry.

- Proper sample handling and shipping/transport techniques.

- Field replicate samples (blind to the laboratory), e.g. 1 replicate/10 samples).

- Field replicate measurements (e.g. 1 replicate measurement/10 field measurements).

Field Replicate samples and Field Replicate measurements should generally be equal to 15% of total field and/or lab measurements or at least 1/sampling event, whichever is greater.  Use Table 13 and revise as appropriate for the project to characterize field QC types, frequency and acceptance criteria limits.

| Table 13: Field Quality Control Samples |
| --- |
| Field Quality Control Sample | Measurement Parameter | Frequency | QC Acceptance Criteria Limits |
|  |  | Frequency of Occurrence | Total # of QC Type Samples |  |
| Field Blank |  |  |  |  |
| Trip Blank |  |  |  |  |
| Field Replicate (Blind to Lab.) |  |  |  |  |
| Field Replicate Measurement |  |  |  |  |
| Calibration Vérification Check Standard |  |  |  |  |

### B.5.2	Laboratory Quality Control (QC) Measures

In this section detail the Laboratory Quality Control Measures including QC samples collected in the field for subsequent laboratory analysis as well as method-specific laboratory QC activities prescribed in each analytical method’s SOP and in the monitoring project’s QAPP. Modify Table 14 as appropriate for the project.

Laboratory QC includes the following:

- Laboratory instrumentation calibrated with the analytical procedure.

- Laboratory instrumentation maintained in accordance with the instrument manufacturer’s specifications, the laboratory’s QAP and Standard Operating Procedures (SOPs).

- Matrix spike/matrix spike duplicates, sample duplicates, calibration verification checks, surrogate standards, external standards, etc. per the laboratory’s QAP and SOPs.

- Specific QC activities prescribed in the project’s QAPP.

- Laboratory data verification and validation prior to sending data results to ADEC and/or permitted facility.

Contracted laboratories will provide analytical results after verification and validation by the laboratory QA Officer.  The laboratory must provide all relevant QC information with its summary of data results so that the project manager and project QA officer can perform field data verification and validation and review the laboratory reports.  The Project Manager reviews these data to ensure that the required QC measurement criteria have been met.  If a QC concern is identified in the review process, the Project Manager and Project QA Officer will seek additional information from the contracted laboratory to resolve the issue and take appropriate corrective action.

| Table 14: Field/Laboratory Quality Control Samples |
| --- |
| Field/Lab Quality Control Sample | Measurement Parameter | Frequency | QC Acceptance Criteria Limits |
|  |  | Frequency of Occurrence | Total # of QC Type Samples |  |
| Field Blank |  |  |  |  |
| Trip Blank |  |  |  |  |
| Field Replicate |  |  |  |  |
| Lab Blank |  |  |  |  |
| Lab Fortified Blank |  |  |  |  |
| Calibration Verification Check Standard |  |  |  |  |
| Continuing Calibration Verification Check Standard |  |  |  |  |
| Matrix Spike/Matrix Spike Duplicate |  |  |  |  |
| Lab Duplicate Sample |  |  |  |  |
| External QC Check Standard |  |  |  |  |
| Surrogate Standard |  |  |  |  |

## B.6	INSTRUMENT/EQUIPMENT TESTING, INSPECTIONAND MAINTENANCE REQUIREMENTS

In this section describe the procedures and criteria used to verify that all instruments and equipment are acceptable for use.

Prior to a sampling event, all sampling instruments and equipment are to be tested and inspected in accordance with the manufacturers’ specifications.  All equipment standards (thermometers, barometers, etc) are calibrated appropriately and within stated certification periods prior to use.

Monitoring staff should document that required acceptance testing, inspection and maintenance have been performed. Records of this documentation should be kept with the instrument/equipment kit in bound logbooks or data sheets.

Contracted and sub-contracted laboratories will follow the testing, inspection and maintenance procedures required by EPA Clean Water Act approved methods and as stated in the respective laboratory’s QAP and SOPs.

## B.7	INSTRUMENT CALIBRATION AND FREQUENCY

Field instruments must be calibrated where appropriate prior to using the instruments.  For example, pH meters must be calibrated according to the manufacturer’s specifications using pH buffers at 4.0, 7.0 (mid-range) and 10.0 that are within their certification period (expiration date has not lapsed).  If equipment and/or kits require calibration immediately prior to the sampling event, the calibration date will be recorded in the operator’s field logbook or field data sheets.  When field instruments require only periodic calibration, the record of this calibration should be kept with the instrument.  The project manager will delegate a field project team member to ensure that instruments are calibrated correctly and appropriate documents recorded and retained.

Contracted and sub-contracted laboratories will follow the calibration procedures found in its QAP and the laboratory’s SOPs.  Specific calibration procedures for regulated pollutants will be in agreement with the respective EPA Approved CWA method of analysis.  Field and/or laboratory calibration records will be made available to ADEC upon request.

## B.8	INSPECTION/ACCEPTANCE OF SUPPLIES AND CONSUMABLES

In this section describe how and by whom supplies and consumables (e.g., standard materials and solutions, filters, pumps, tubing, sample bottles, glassware, reagents, calibration standards, electronic data storage media, etc.) are inspected and accepted for use in the monitoring project.

All reagents, calibration standards, and kit chemicals are to be inspected to ensure that expiration dates are not exceeded prior to use in the monitoring project.

All sample collection devices and equipment will be appropriately cleaned prior to use in the monitoring project.

All sample containers, tubing, filters, etc. provided by a laboratory or by commercial vendor will be certified clean for the analyses of interest.  The sampling team will take note of the information on the certificate of analysis that accompanies sample containers to ensure that they meet the specifications and guidance for contaminant-free sample containers for the analyses of interest.

No standard solutions, buffers, or other chemical additives shall be used if the expiration date has passed.  The sampling manager or his/her designee is responsible to maintain appropriate records (e.g. logbook entries, checklists, etc.)  to verify inspection/acceptance of supplies and consumables, and restock these supplies and consumables when necessary.

Contracted and sub-contracted laboratories will follow procedures in their laboratory’s QAP and SOPs for inspection/acceptance of supplies and consumables.

## B.9	DATA ACQUISITION REQUIREMENTS (NON-DIRECT MEASUREMENTS)

In this section identify the type of data needed for project implementation or decision-making obtained from non-measurement sources such as maps, charts, GPS latitude/longitude measurements, computer data bases, programs, literature files and historical data bases.  Describe the acceptance criteria for the use of such data and specify any limitations to the use of the data.  If data of known and accepted quality is to be modeled to predict water quality impacts, the specific model of use is to be identified, referenced and justified.

## B.10	DATA MANAGEMENT

The success of a monitoring project relies on data and their interpretation.  It is critical that data be available to users and that these data are:

- Of known quality,

- Reliable,

- Aggregated in a manner consistent with their prime use, and

- Accessible to a variety of users.

Quality Assurance/Quality Control (QA/QC) of data management begins with the raw data and ends with a defensible report, preferably through the computerized messaging of raw data.

Data management encompasses and traces the path of the data from their generation to their final use or storage [e.g., from field measurements and sample collection/recording through transfer of data to computers (laptops, data acquisition systems, etc.), laboratory analysis, data validation/verification, QA assessments and reporting of data of known quality to the respective ADEC Division of Water Program Office].  Data management also includes/discusses the control mechanism for detecting and correcting errors.

In this section include a flow chart as well as a detailed narrative of the monitoring project’s data management process.  An example Data Management Flow Chart (Figure 2) at the end of this section provides a visual summary description of the data flow/management process for environmental data collected in support of ADEC’s Division of Water.  Revise Figure 2 as appropriate for the specific monitoring project.

Various people are responsible for separate or discrete parts of the data management process:

- The sampling team is responsible for field measurements/sample collection and recording of data and subsequent shipment of samples to laboratories for analyses. They assemble data files, which includes raw data, calibration information and certificates, QC checks (routine checks), data flags, sampler comments and meta data where available. These files are assembled and forwarded for secondary data review by the sampling manager or supervisor.

- Laboratories are responsible to comply with the data quality objectives specified in the QAPP and as specified in the laboratory QAP and method specific SOPs.  Validated sample laboratory data results with respective analytical method QA/QC results and acceptance criteria are reported to the sampling manager or project supervisor. It is recommended that analytical data is submitted in pdf and as an electronic data deliverable (EDD).

- Secondary reviewers (sampling coordinator/supervisor/project supervisor) are responsible for QA/QC  review, verification and validation of field and laboratory data and data reformatting as appropriate for reporting to STORET, AQMS, ICIS-NPDES, DROPS (if necessary), and reporting validated data to the project manager.

- The project QA officer is responsible for performing routine independent reviews of data to ensure the monitoring projects data quality objectives are being met. Findings and recommended corrective actions (as appropriate) are reported directly to project management.

- The project manager is responsible for final data certification

- DEC DOW Project Manager/WQAO conducts a final review (tertiary review) and submits the validated data to STORET, AQMS, ICIS-NPDES, DROPS as appropriate.

## B.11         Data Storage and Retention

Data management files will be stored on a secure computer or on a removable hard drive that can be secured.  Laboratory records must be retained by the contract laboratory for a minimum of five years. Project records must be retained by the lead organization conducting the monitoring operations for a minimum of five years, preferably longer. Site location and retention period for the stored data will be specified in Section A9, Documents and Records, Table 8.

Figure 2:  Example Data Management Flow Chart

# C.	 ASSESSMENTS

## C.1	ASSESSMENTS AND RESPONSE ACTIONS

In this section describe in detail the type, number and frequency and acceptance criteria for each type of assessment scheduled for the monitoring project.  Revise Table 15 as appropriate to summarize the scheduled project assessment types, number, frequency and acceptance criteria limits.

Use the following guidance to design the appropriate QA assessment activities for a Tier 2 Water Quality Monitoring QAPP.  Each monitoring project is different, with different intended data uses, different parameters to be measured and different project budgets.  The key is to design an appropriate strategy to evaluate the overall monitoring system (data collection, analysis and reporting) with some level of confidence to independently substantiate the end-use quality data required by the monitoring project.

Assessments are independent (of management) evaluations of the monitoring project that are performed by the Project’s QA Officer or his/her designee.  For Tier 2 QAPPs, assessments may include, but are not limited to, any of the following:  on-site field surveillance, on-site laboratory audits, performance evaluation samples, DMRQA samples, blind sample replicates (precision samples), field split samples, data quality audits, and data reviews.  The number and types of assessments are dependent upon the monitoring project’s intended data uses.

C.1.1	Tier 2 Monitoring Data Assessment

Generally, monitoring projects requiring high end-use quality data results for comparison to Alaska’s water quality standards  (e.g., compliance monitoring, listing/de-listing of impaired waters, etc.) need more frequent and varied assessments to provide a more thorough and independent validation that the monitoring project did actually capture high end-use quality data.  Monitoring projects collecting samples for subsequent laboratory analysis need more types of assessments than just project field measurements to independently evaluate the overall monitoring system.

Example QA Assessments are:

Field Assessments (each pollutant)

- Precision (replicate) sample measurements.  Project should have minimum of three paired measurements/project or 10% of project samples, whichever is greater.  Replicate measurements should be evenly spaced over project timeline. Precision criteria are specified in the project’s Measurement Quality Objectives (MQO) table, see section A7.

Field samples collected for subsequent laboratory analysis (each pollutant)

- Blind replicate samples for each pollutant to be measured.  Project should have minimum of three paired measurements/project or 10% of project samples, whichever is greater.  Replicate samples should be evenly spaced over project timeline. Precision criteria are specified in project’s MQO table, see section A7.

- Sample splits (one split sent to lab analyzing project samples, other split sent to a reference lab).

- Matrix spike duplicates (MSD) (assesses total measurement bias for project – both precision and accuracy). Frequency of MSDs is usually specified by the analytical method.  Accuracy and precision of criteria for each pollutant and analytical method are specified in the project’s MQO table, see section A7.

- Third party performance evaluation samples (PE samples also called performance test (PT) samples) for wastewater analytes of interest.  PT water/wastewater sample participation is at a frequency of 1/year from a NELAC certified vendor (http://nelac-institute.org/abdb.php ).  For APDES permit monitoring, these are called DMRQA samples.

Microbiological samples must be analyzed by a current DEC Division of Environmental Health Drinking Water certified lab (http://dec.alaska.gov/applications/eh/ehllabreports/certmicrolabs.aspx) for the methods of interest.  For those microbiological methods not covered under the DEC EH Lab DW certification program, the microbiological lab will enroll in an approved PT study for the microbiological method of interest (see above link for approved NELAC PT vendors).  Laboratory third party microbiological PT samples results will be submitted directly to the DEC Water QA Officer and the Monitoring Project’s QA Officer.

On-Site Assessments

- Inspection of field monitoring operations for compliance with QAPP requirements.

- Laboratory Audit (if concerns arise regarding laboratory data quality)

- Audit of project field measurement data results.

Project Data Assessments

- Audits of Monitoring Data for reproducibility of results from recalculation/reconstruction of field/lab unprocessed data.

- Calculation of monitoring project’s overall achieved precision, accuracy and data completeness compared to QAPP defined precision, accuracy and data completeness goals.

| Example Table 15 Project Assessments |
| --- |
| Assessment Type | Measurement Parameters | Frequency | Acceptance Criteria Limits |
|  | Analyte | Method |  |  |
| On-site Field Audit/Inspection | XXXX | XXXX | 1/site/monitoring season | Site technicians in compliance with QAPP sampling protocols, sample sites meet sample design criteria |
| 3rd Party Blind PT/DMR QA Sample (Lab) | XXXX | XXXX | annually | Analytes within PT study limits |
| Field Split Sample (sent to different labs for comparison analysis) |  |  |  |  |
| On-site Technical System Lab audit |  |  |  |  |
| Independent Data Review Audit | XXXX | XXXX | 10% of reported data | XXXX |
| Project Precision, Accuracy and Data Completeness Assessment | XXXX | XXXX | end of project and at least 1/year | Defined in Section A7 and Table 6 |

## C.2	REVISIONS TO QAPP

Annually the QAPP will be reviewed and revised as needed by the project manager and the project QA officer.   Minor revisions may be made without formal comment.  Such minor revisions may include changes to identified project staff (but not lead project staff: QA project officer, project manager, sampling manager, contracted laboratories), QAPP distribution list and/or minor editorial changes.

Revisions to the QAPP that affect stated monitoring Data Quality Objectives,  Measurement Quality Objectives, method specific data validation “critical” criteria and/or inclusion of new monitoring methods must seek review and pre-approval by DEC DOW QA Officer/DEC Project Management before being implemented.

## C.3	QA REPORTS TO MANAGEMENT

Use Table 16 to describe assessment types, frequency, content, responsible individual/s, and distribution of assessment reports to management and other recipients and actions to be taken.  Revise as appropriate to list project QA assessments.

| Example Table 16: QA Reports to Management |
| --- |
| QA Report Type | Contents | Presentation Method | Report Issued by | Reporting Frequency |
|  |  |  |  | As Required | Year |
| On-site Field Inspection Audit Report | Description of audit results, audit methods and standards/equipment used and any recommendations | Written text and tables, charts, graphs displaying results | Project QA Officer/auditor | ( |  |
| Field Split Sample Report | Evaluation/comparison of result of split sample results from different laboratories, audit method | Written text and tables, charts, graphs displaying results | Project QA Officer/auditor | ( |  |
| On-site Laboratory Audit Report | Description of audit results, audit methods and standards/equipment used and any recommendations | Written text and tables, charts, graphs displaying results | Project QA Officer/auditor | ( |  |
| 3rd Party PT (DMRQA, etc.) Audit Report | Description of audit results, methods of analysis and any recommendations | Written text and charts, graphs displaying results | Project QA Officer/auditor | ( | ( |
| Corrective Action Recommendation | Description of problem(s), recommended corrective action(s), time frame for feedback on resolution of problem(s) | Written text/table | QA Officer/auditor | ( |  |
| Response to Corrective Action Report | Description of problem(s), description/date corrective action(s) implemented and/or scheduled to be implemented | Written text/table | Project Manager overseeing sampling and analysis | ( |  |
| Data Quality Audit | Independent review and recalculation of sample collection/analysis (including calculations, etc) to determine sample result. Summary of data audit results; findings; and any recommendations | Written text and charts, graphs displaying results | Project QA Officer | ( |  |
| Quality Assurance Report to Management | Project executive summary: data completeness, precision, bias/accuracy | Written text and charts, graphs displaying results | Project QA Officer | ( | ( |

# D.	DATA VALIDATION AND USABILITY

## D.1	DATA REVIEW, VERIFICATIONAND VALIDATION REQUIREMENTS

The purpose of this section is to define the criteria used to review and validate monitoring data-that is, accept, reject or qualify data in an objective and consistent manner.  Data review, verification and validation is a way to decide the degree to which each data item has met its quality specifications (i.e. analyte specific QC criteria and overall project measurement quality objectives).

### D.1.1	Data validation

Data validation means determining if data satisfy QAPP-defined user requirements, that is, that the data refer back to the overall data quality objectives.  Data validation is an analyte and sample-specific process that extends the evaluation of data beyond method, procedural, or contractual compliance (i.e., data verification) to determine the analytical quality of a specific data set to ensure that the reported data values meet the quality goals of the environmental data operations (analyte and method specific data validation criteria).

### D.1.2	Data Verification

Data verification is the process of evaluating the completeness, correctness, and conformance/compliance of a specific data set against the method, procedural, or contractual requirements.

### D.1.3	Data Review

Data review is the process that evaluates the overall data package to ensure procedures were followed and that reported data is reasonable and consistent with associated QA/QC results.

## D.2	VERIFICATION AND VALIDATION METHODS

In this section describe the project’s specific procedures for validating and verifying data.  Discuss how issues are resolved and identify the authorities for resolving such issues.  Describe how the results are to be conveyed to the data users.  This section should reference examples of QAPP forms and checklists, which could be provided in the appendices.  Any project-specific calculations are identified in this section.

### D.2.1	Validation Methods

Data validation determines whether the data sets meet the project-specific requirements as described in the QAPP.  That is, were the data results of the right type, quality, and quantity to support their intended use.  Data validation also attempts to give reasons for sampling and analysis anomalies, and the effect that these anomalies have on the overall value of the data.

All data generated shall be validated in accordance with the QA/QC requirements specified in the methods and the technical specification outlined in this QAPP.  Raw sample data will be maintained by the agency or company responsible for the monitoring project.  Raw laboratory data shall be maintained by the laboratory.  The laboratory may archive the analytical data into their laboratory data management system.

The summary of all laboratory analytical results will be reported to the project manager.  Data validation will be performed by the laboratory for all analyses prior to the release of data.  All laboratory data will be validated according to the laboratory’s QAP and SOPs and, as specified in the Monitoring Project’s QAPP.  The rationale for any anomalies in the QA/QC of the laboratory data will be provided to the Project Manager with the data results.  Completed COC or transmission forms (if required) will be sent back from the laboratory to the Project Manager.

Data will be qualified as necessary. Unacceptable data (i.e., data that do not meet the QA measurement criteria of precision, accuracy, representativeness, comparability and completeness) will not be used or if used, the problems with the data will be clearly defined, flagged appropriately and data use clearly delimited and justified.  Any actions taken to correct QA/QC problems in sampling, sample handling, and analysis must be noted.  Under the direction of the Project Manager, project staff will document any QA/QC problems and the respective QA/QC corrective actions taken.

The Project Manager/monitoring supervisor or his/her designee is responsible for reviewing field log notebooks and field data sheets for accuracy and completeness within 48 hours of each sample collection activity, if possible.  Sample results provided by the laboratory will be verified and validated by the laboratory QA Officer prior to issuing the laboratory report.  Laboratory results will include the results of all QA/QC results as part of the sample data report. The laboratory report will become part of the permanent file for the monitoring project.  The Project Manager or his/her designee will compare the sample information in the field log notebooks and/or data field sheets with the laboratory analytical results to ensure that no transcription errors have occurred and to verify project QA/QC criteria have been met (e.g., relative percent difference (RPD) results for blind sample duplicates, percent analyte recovery results for matrix spike and matrix spike duplicate (MS/MSD) results, etc).

The Project QA Officer or his/her designee will calculate the RPD between field replicate samples.

Laboratories calculate and report the RPD and percent analyte recovery of analytical duplicate samples and MS/MSD samples.

Analyte specific precision, accuracy and data completeness results greater than project MQO’s will be noted by the Project Manager and justified in the final data report.  The Project Manager, along with supervisors and/or the Project QA Officer, if necessary, will decide if any QA/QC corrective action is necessary if the precision, accuracy (bias) and data completeness values exceed the project’s MQO goals.

### D.2.2	Verification Methods

The primary goal of verification is to document that applicable method, procedural and contractual requirements were met in field sampling and laboratory analysis.  Verification checks to see if the data is complete, if sampling and analysis matched QAPP requirements, and if Standard Operating Procedures (SOPs) were followed.

## D.3	RECONCILIATION WITH USER REQUIREMENTS

The Project Manager and the Project QA Officer will review and validate data against the Project’s defined MQOs prior to final reporting stages.  If there are any problems with quality sampling and analysis, these issues will be addressed immediately and methods will be modified to ensure that data quality objectives are being met. Modifications to monitoring that affect the quality of reported data will require notification to and pre-approval by ADEC as well as subsequent edits to the approved QAPP.

Only data that have been validated, verified and qualified, as necessary, shall be submitted to ADEC Division of Water and entered into the applicable database (STORET, AQMS, ICIS-NPDES, DROPS).

# Text boxes

Management Direction

Data Reporting

QA Assessment/Reporting

Figure 1:	Example Project Organizational Structure

ADEC DOW

Project Manager

ADEC DOW

QA Officer

DEC DOW Data Base (AWQMS, DROPS)

Field Sampling

Laboratory

Sampling & Analysis Manager

Project Manager

Project QA Officer

Field Staff Supervisor

100% check of all data, logbooks, field data sheets & initial data flags, providing flag rational

Project QA Officer

Minimum 10% random check of all data, 100% check of all elevated values and outlier values. Verify QAPP & SOP compliance Verify and validate flags, SOP procedural adjustment & Recommendations.  Assess attainment of overall project required MQOs

Field Staff Operator Data Management Responsibilities

Maintains all log books, field data sheets, QC forms

Calculates concentrations as needed, Conducts preventative maintenance, calibrations and QC checks.  Ensures all test equipment is in certification and all SOPs are followed.

Field Data

Data is collected and recorded on forms, logbooks computer files and concentrations calculated

Analytical Laboratory

100% check of all field sample request data sheets, sample integrity checks (preservation, temperature and holding times met).  Samples analyzed according to QAPP approved methods.  Sample analysis and relevant QC results reported.

Project Supervisor

Data review and 10% check of all field and laboratory data (field notes, sample field and lab results, QC data verification/validation and appropriate use of data flags)

Project Manager

Review Data. Report sample data results per QAPP requirements,

Data Management Legend

Data reporting

QA Assessments

Data not okay or needs more info

DEC

Division of Water

Project Manager/QA Officer

Reviews Data for acceptability

STORET, DROPS, ICIS-NPDES, AWQMS