## Slide 1
Juneau Air Quality and Cruise ship Emissions Monitoring
DEPARTMENT OF ENVIRONMENTAL CONSERVATION DIVISION OF AIR QUALITY and DIVISION OF WATER QUALITY
January 29, 2019
1

## Slide 2
Who at DEC Monitors Cruise Ships?
Cruise Ships
Wastewater
Air
Opacity
Ambient Air Quality
Yellow – Division of Water Quality; Cruise Ships – Ed White
Green – Division of Air Quality; Air Monitoring- Barbara Trost

## Slide 3: 2018 Concerns and Questions
Public complaints and questions
  Large increase in 2017 and 2018
  Complaints from outside Juneau
  Types of complaints
  Increase in ship traffic and size of ships
  Changes in ship operations

## Slide 4: Public concerns and questions

## Slide 5: Opacity
All ships must comply with State’s Opacity limits
State of Alaska has been monitoring vessel air emissions since 1970s

## Slide 6
Ambient Air Quality
In 2000 an Ambient Air Quality study was conducted in Juneau due to concern about cruise ship opacity.
  No exceedances of air quality standards were found in the 2000 study

## Slide 7
Information
DEC Cruise Ship website https://dec.alaska.gov/water/cruise-ships/

## Slide 8
Cruise Ship Industry Impact on Air Quality
DEPARTMENT OF ENVIRONMENTAL CONSERVATION DIVISION OF AIR QUALITY and DIVISION OF WATER QUALITY
January 29, 2019
1

## Slide 9: 2019 Ambient Air Quality Screening Level Study
  Objectives:
  To address ambient air quality complaints centered on the cruise ship emissions
  To determine which areas of downtown Juneau are most affected
  To assess if the scale in terms of frequency, duration, spatial variability and severity of these impacts have the potential to significantly affect public health and/or violate Clean Air Act air quality standards.

## Slide 10
2019 Ambient Air Quality Saturation Study
Saturation study:
study floods a small area with a large number of low-cost non-regulatory sensors for a short period of time, typically to answer a defined set of questions
• 20 non-regulatory PM2.5 sensors set up in a grid in downtown area
• 10 non-regulatory passive SO2 samplers at selected sites on days with many cruise ships in port
• Site selections yet to be made: city and state buildings; volunteers
• Results of screening level study and available funding will determine future actions.

## Slide 11
Saturation Study Equipment
PM2.5  Purple Air
    Continuous
    Non-regulatory
    Posts real-time data on website
    20 sites –
      Mar-May 2019 pre season
      Jun –Oct 2019 maximum impact
SO2  Ogawa Passive Sampler
    Integrated (12-24 hours)
    Non-regulatory
    Detection limit (24 hours) ~3.8 ppb (depends on lab analysis)
    10 sites; 2 per week for 4 weeks

## Slide 12: Access to data
Purple Air PM2.5
• Wireless communication & SD cards
• DEC will develop website for the study
• May look something like this
• Still in planning phase
Ogawa Passive SO2 monitors
• Not ‘real time’
• Exposed 12 - 24 hours
• Wait for lab analysis

## Slide 13: Preliminary monitoring plan
Background Monitoring
Before the start of the cruise ship season on April 28, 2019
Purple Air:
  grid pattern covering downtown Juneau
  Power cost ~ $1/ month
  Operating entire study period
Passive SO2 sampler :
  3 days chosen to have similar weather conditions to expected ‘worst’ days
Plume identification monitoring
• Passive Ogawa SO2 monitoring
  Located at a subset of Purple Air sites
  Targeted sampling at days with large number of cruise ships in port (example 6 cruise ships in port on 5/28/19)
  No power required

## Slide 14: Passive Ogawa SO2 monitoring
Targeted at days with large number of cruise ships in port (example 6 cruise ships in port on 5/28/19)

## Slide 15: Example Sensor Grid
PM2.5 sensor locations
(Purple Air)
SO2 samplers will be collocated with some of the Purple Air sensors

## Slide 16: Help us help you…
Add information to the laminated map with sticky flags
Are you willing to host a monitor?
Contact us!
Barbara Trost
AMQA Program Manager
barbara.trost@alaska.gov
907-269-6249
Anna Breuninger
Saturation Study Coordinator
anna.breuninger@alaska.gov
907-269-7573
…. please leave your name, phone number, email and address & location proposed on the green signup sheet

## Slide 17: Commercial Passenger Vessel Environmental Compliance Program “Cruise Ship Program” January 29, 2019
Large Cruise Ships (>250 passengers)
  Small Cruise Ships (50 to 249 passengers)
  Alaska State Ferries

## Slide 18: Background Information
18 AAC 50.070 – Marine Vessel Visible Emission Standards
Exemptions are granted for initial startup & maneuvering
EPA Reference Method 9

## Slide 19: Opacity Limits
18 AAC 50.070. Marine vessel visible emission standards
1)(A) While vessel is at berth or anchor (over 20% for up to three minutes )
(1)(B) While vessel is at berth during initial startup of the vessel preparing to cast off or weigh anchor (over 20% for up to six minutes)
(2)During the hour immediately after weighing anchor or casting off (up to 40% for an hour or up to 100% for nine minutes)
(3) During the hour before completion of maneuvering to anchor or making fast to shore (up to 40% for an hour or up to 100% for nine minutes)
(4)Vessel underway and not covered under 1-3 above (over 20% for up to three minutes )

## Slide 20: Opacity Monitoring of Cruise Ships & State Ferries

## Slide 21: Opacity Monitoring Program
ADEC staff
ADEC Contractor
  Minimum of 225 reading per cruise ship season
US Forest Service Rangers
Address Public Complaints
  Conduct a Method 9
  Contact the cruise line
Self-monitor (Continuous Emissions Monitoring)
Self-report under 18 AAC 50.240

## Slide 22: Opacity Monitoring in 2018
Port | Number of Readings
Anchorage | 2
Haines | 2
Hoonah | 2
Juneau | 233
Ketchikan | 196
Seward | 3
Sitka | 16
Skagway | 26
Wrangell, AK | 3
DEC and Contractor Opacity Reading Count by Port (2018)
Opacity Readings Per Year Summary
Year | 2014 | 2015 | 2016 | 2017 | 2018
Number of Readings | 382 | 343 | 388 | 552 | 480

## Slide 23
Opacity Enforcement in 2018
5
Opacity Enforcement Action Per Year Summary
Year | 2010- 2014 | 2015 | 2016 | 2017 | 2018
Violations | 49 | 0 | 0 | 2 | 9
Settlement totals | $533,125 | $0 | $0 | $75,000 | TBD
Vessel | Date | Port | Status
HAL Nieuw Amsterdam | 6/19/18 | Skagway | Pending
HAL Westerdam | 6/20/18 | Haines | Pending
NCL Norwegian Jewel | 7/11/18 | Ketchikan | Settled
PCL Emerald Princess | 7/31/18 | Ketchikan | Pending
PCL Golden Princess | 7/31/18 | Juneau | Pending
HAL Eurodam | 8/2/18 | Ketchikan | Pending
RCL Radiance of the Seas | 8/8/18 | Ketchikan | Pending
RCL Radiance of the Seas | 8/17/18 | Seward | Pending
HAL Amsterdam | 8/24/18 | Ketchikan | Pending
Opacity Violations Issued (2018)

## Slide 24: Questions?
Contact us!
Ed White
CPVEC Program Manager
edward.white@alaska.gov
907-465-5138
Denise Wiltse
Program Specialist
denise.wiltse@alaska.gov
907-465-5278