## Slide 1: CHAPTER 4
Water Sources and Treatment Options

## Slide 2: Water Supply Hydrology
Hydrology: The science dealing with the properties, distribution, and circulation of water and its constituents in the atmosphere, on the earth’s surface, and below the earth’s surface.
The Hydrologic Cycle: The movement of water to and from the surface of the earth.

## Slide 3: The Hydrologic Cycle
Copyright © 2016 the American Water Works Association

## Slide 4: The Hydrologic Cycle: Terminology
Evaporation – water moving from the surface to the atmosphere
Transpiration – water released from plants to the atmosphere
Evapotranspiration – combination of evaporation and transpiration
Sublimation – ice and snow evaporating directly into the atmosphere
Advection – water movement in the atmosphere by air currents
Condensation – formation of water droplets
Precipitation – rain, snow, sleet, hail, etc.
Notes: Evapotranspiration is a term occasionally used in exam questions that is the combination of the terms evaporation and transpiration

## Slide 5: The Hydrologic Cycle: Terminology
Interception – precipitation that encounters plants rather than soil
Infiltration – precipitation that soaks into the ground
Subsurface Flow – movement of water through the soil
Runoff – water that flows over the surface of the ground
Channel Flow – runoff that collects in streams and rivers
Storage – water that is stored in surface lakes and reservoirs, frozen in snow and ice, or held in subsurface aquifers (saturated zones)
Snowmelt – water released as snow and ice packs melt in the spring

## Slide 6: Groundwater
Groundwater accumulates as infiltration water percolates down to a water table
An aquifer is a saturated subsurface zone
The water table is the surface of the saturated layer in an aquifer
Copyright © 2016 the American Water Works Association

## Slide 7: Aquifers and Confining Beds
Unconfined Aquifers:
  The surface of the saturated zone is free to rise or fall with precipitation and snowmelt events
  The top of the saturated zone is called the water table
Copyright © 2016 the American Water Works Association

## Slide 8: Aquifers and Confining Beds
Copyright © 2016 the American Water Works Association
Confined (Artesian) Aquifers:
  A permeable layer is confined between upper and lower layers with low permeability
  The confining layers are called aquitards or aquicludes, and consist of bedrock, clay, or permafrost
  Artesian aquifers are recharged from a higher elevation and are under pressure
  The height to which water rises in an artesian aquifer is called the piezometric surface
Notes: A number of artesian aquifers in Alaska are located beneath confining permafrost layers such as in the Yukon-Kuskokwim Delta (Bethel area) where the aquifer is beneath ~300 feet of continuous permafrost

## Slide 9: Aquifer Materials
Copyright © 2016 the American Water Works Association
Aquifers are made up of a variety of water-bearing materials (Figure 4-6)
Porosity: the amount of water that the material in the aquifer can hold
Permeability: the ease with which water flows through the aquifer materials (also known as hydraulic conductivity)
Notes: Note: permeability also impacts the rate at which an aquifer recharges while a well is being pumped and after the pump has been shut down.

## Slide 10: Groundwater Movement
Copyright © 2016 the American Water Works Association
Water moves downhill (down gradient) in an aquifer and may be at different levels as in Figure 4-7
Water may flow into a stream if the water table is higher than the stream stage level (elevation) as shown in Figure 4-8
Copyright © 2016 the American Water Works Association
Notes: Some aquifers in Alaska are “perched” aquifers, located above a permafrost layer. If the permafrost thaws the aquifers may disappear, draining out through the newly thawed zone.

## Slide 11: Springs
Copyright © 2016 the American Water Works Association
Springs occur where the water table intersects the surface of the ground – hydrologists refer to this as “daylighting”
Springs may be true groundwater, being recharged from a more distance source, or groundwater under the influence of surface water, being recharged from a nearby location

## Slide 12: Video Clip: Aquifers
www.awwa.org/wsovideoclips

## Slide 13: Surface Water
Surface water is water that is in contact with the atmosphere and results from overland flow
Surface water includes lakes, streams, rivers, surface impoundments (reservoirs), shallow springs and wells, sea water
Volume and chemical quality varies with the season and weather (precipitation events, snowmelt, wind action, ice scouring, etc.)
Contaminants can flow into the surface water from the ground during runoff, and can accumulate from activities in and around the watershed (see Table 4-1 for the chemical composition of rain water)
Notes: Background photo: Isatkoak Reservoir – Barrow Utilities & Electric Coop, Inc. (BUECI). The salinity of this supply increases significantly during the winter as fresh water is lost to ice formation.

## Slide 14: Groundwater Augmentation of Surface Water
If the water table is higher than the stream, groundwater flows into the stream. This is referred to as a “gaining stream.” (Figure 4-10)
If the water table is lower than the stream, water flows from the stream into the aquifer. This is a ”losing stream.” (Figure 4-11)
Copyright © 2016 the American Water Works Association

## Slide 15: Surface Runoff
Copyright © 2016 the American Water Works Association
The drainage basin or watershed is the land surface that contributes water to the streams and water bodies in that area
Watercourses include naturally-occurring creeks, streams, and rivers and human constructed ditches, channels, canals, aqueducts, conduits, tunnels and storm sewers

## Slide 16: Video Clip: Surface Water Sources
www.awwa.org/wsovideoclips

## Slide 17: Introduction to Water Treatment
Health-Related Treatment: water is treated to the requirements of the safe drinking water act for microbiological, chemical, and radiological contaminants that have health effects
  The resulting water is referred to as “Potable”
Aesthetic-Related Treatment: water is treated for secondary contaminants that affect the appearance, taste, odor, and other non health-related qualities of water
  The resulting water is referred to as “Palatable”
Treatment Required by Regulation: the Safe Drinking Water Act requires minimum levels of treatment for different types of water sources such as surface water and groundwater
Notes: Background photo: Golden Heart Utilities (GHU) 8-MGD lime softening groundwater treatment plant in Fairbanks – solids contact basin #2 operating.

## Slide 18: Water Treatment Process Selection
Water Treatment Design Considerations:
  Water supply source: groundwater versus surface water
  Required finished water quality
  Capital and operating costs
  Process footprint versus land availability
  Residuals disposal
  Applicability to the multiple-barrier approach

## Slide 19: Groundwater Sources
Advantages:
  Microbiological content is lower than surface water
  Quality and temperature remain relatively constant
Disadvantages:
  Higher mineral content (e.g. higher hardness levels, iron and manganese)
  Persistent contaminants may be present in aquifers (e.g. fuels, solvents, synthetic organic chemicals)
  Pumping costs are usually higher than surface water
  Virus removal (disinfection) may be required by the Groundwater Rule
Groundwater well with a vertical turbine pump

## Slide 20: Surface Water Sources
Advantages:
  Usually more accessible than groundwater, lower pumping costs
  Information on quantity and quality is easier to obtain than groundwater
Disadvantages:
  More easily contaminated than groundwater
  Susceptible to algae blooms that can cause tastes, odors, and some toxicity
  Quality and quantity can change rapidly requiring treatment adjustments
  All surface water must be treated in accordance with the Surface Water Treatment Rules
Surface water reservoir gravity dam spillway

## Slide 21: Multiple-Barrier Approach
The Multiple-Barrier Approach provides a relatively fail-safe system to water quality management for water utilities through the following elements:
  Source water (watershed) protection
  Provide appropriate and adequate treatment such as filtration and disinfection for surface water sources
  Maintain water quality throughout the storage and distribution system
  Provide adequate monitoring for regulated water quality parameters to ensure treated water is potable and palatable
  Professional system operations including good business management and operator certification

## Slide 22: Selection of Treatment Methods
The types of treatment methods used depends on the type and quality of source water, and may include any of the following, which will be reviewed in future chapters of this course:
  Air stripping, aeration, and or chemical oxidation
  Coagulation process, mixing and flocculation
  Ion exchange
  Chemical precipitation
  Membrane processes
  Disinfection
  Absorption
  Proper disposal of treatment residuals and waste streams